## Slide 1: Descriptive and inferential statistical methodologies have proven effective in creating a proactive ‘alarm’, accurately identifying Pump Failures with Horse Power (HP) and Pump Efficiency (PE) emerging as key variables of interest with deviations of 15 HP and > 3 % PE being our core signal thresholds.
Chart: Statistical Alarm Plot
PUMP FAILURE (1 or 0) |  | 
Raw Data | Correlation Coefficient | 
Volumetric Flow Meter 2 | -0.11211472 | 
Pump Efficiency | -0.102684351 | 
Volumetric Flow Meter 1 | -0.102508317 | 
Ambient Temperature | 0.20794584 | 
Pump Torque | 0.233192706 | 
Pump Speed (RPM) | 0.260016062 | 
Horse-Power | 0.421844074 | 
PUMP FAILURE (1 or 0) | Rolling Mean (30 Minute) Correlation Coefficient
Volumetric Flow Meter 2 | -0.697731416
Pump Efficiency | -0.695027831
Volumetric Flow Meter 1 | -0.692425138
Ambient Temperature | -0.302615535
Pump Torque | -0.215937441
Pump Speed (RPM) | -0.184159622
Horse-Power | 0.218050641
PUMP FAILURE (1 or 0) | 
Rolling Stdev (30 Minute) | Correlation Coefficient
Pump Torque | 0.597260414
Ambient Temperature | 0.600050431
Pump Speed (RPM) | 0.624555908
Volumetric Flow Meter 2 | 0.625920871
Pump Efficiency | 0.64
Volumetric Flow Meter 1 | 0.64
Horse Power | 0.69

## Slide 2: Descriptive Analysis has enabled us to clearly identify particular signature abnormalities showing clear signature changes in both Rolling Standard Deviation and Rolling Mean Datasets when observed over the respective failure period of interest.
Chart: DRT Rolling Mean Line plot for all variables
Chart: DRT Rolling STD DEV plots for all variables

## Slide 3: Plots show a clear signature difference between that of normal behaviour and that of Failure with pump torque, pump speed, and pump efficiency showing the 3 largest variances.

## Slide 4: Correlation analyses across datasets yield particularly interesting insights with pump efficiency and Volumetric Flow Meter 1 negatively correlated with Pump Failure in the Rolling Mean Data, whilst pump efficiency and Volumetric Flow Meter 1 show a subsequently strong positive correlation in the Rolling STDEV Dataset.
Chart: Correlation Strength Associated With Pump Failure (Rolling STDEV)
| Correlation Coefficient
Pump Torque | 0.59726
Ambient Temperature | 0.60005
Pump Speed (RPM) | 0.62456
Volumetric Flow Meter 2 | 0.62592
Pump Efficiency | 0.64355
Volumetric Flow Meter 1 | 0.64488
Horse Power | 0.6901
Chart: Correlation Strength Associated With Pump Failure (Rolling Mean)
| Rolling Mean (30 Minute) Correlation Coefficient
Volumetric Flow Meter 2 | -0.69773
Pump Efficiency | -0.69503
Volumetric Flow Meter 1 | -0.69243
Ambient Temperature | -0.30262
Pump Torque | -0.21594
Pump Speed (RPM) | -0.18416
Horse Power | 0.21805
Chart: Correlation Strength Associated With Pump Failure (RAW DATA)
| Correlation Coefficient
Volumetric Flow Meter 2 | -0.11211
Pump Efficiency | -0.10268
Volumetric Flow Meter 1 | -0.10251
Ambient Temperature | 0.20795
Pump Torque | 0.23319
Pump Speed (RPM) | 0.26002
Horse Power | 0.42184

## Slide 5: Lastly, analysis of the statistical significance of variables contributing towards Pump Failure reveal that with a R Squared of 0.778, a linear model is a good fit for the data with both Rolling Mean and Rolling Standard Deviation datasets contributing key information to understand Pump Failure mechanics.
Variable | P-Value Significance
Horse Power | 3.5524E-219
Volumetric Flow Meter 2 | 2.033E-174
Pump Efficiency | 2.592E-152
Pump Torque | 1.0551E-102
Intercept | 8.27258E-24
Pump Speed (RPM) | 1.68299E-19
Ambient Temperature | 4.20516E-09
Volumetric Flow Meter 1 | 4.01554E-07